## Slide 1
Medical Imaging Final Report
Qiong-Wen
Date: January 6, 2021

## Slide 2: Outline
1. Radon Transform
2. Filter Back Projection
3. GUI design

## Slide 3: Radon transform
Rotate Image
theta = np.arange(0, 181, dTheta=1)
for n in range(numAngles): rotImgObj = img.rotate(-theta[n], resample=Image.BILINEAR) im1.set_data(rotImgObj) sinogram[:, n] = np.sum(rotImgObj, axis=0) # normalize value sino = Image.fromarray((sinogram - np.min(sinogram)) / np.ptp(sinogram) * 255)

## Slide 4
Radon transform-rotation
Zero Padding Image:
MxN
x1, y1 | x2, y2 | x3, y3
x4, y4 | x5, y5 | x6, y6
x7, y7 | x8, y8 | x9, y9
Clockwise Rotation
X’1, y’1 | X’2, y’2 | X’3, y’3
X’4, y’4 | X’5, y’5 | X’6, y’6
X’7, y’7 | X’8, y’8 | X’9, y’9
Img(X’1, y’1) | Img(X’2, y’2) | Img(X’3, y’3)
Img(X’4, y’4) | Img(X’5, y’5) | Img(X’6, y’6)
Img(X’7, y’7) | Img(X’8, y’8) | Img(X’9, y’9)

## Slide 5: back projection
+

## Slide 6: back projection
for n in range(numAngles): Xrot = X * np.cos(theta[n]) + Y * np.sin(theta[n]) XrotCor = np.round(Xrot + imageLen / 2) XrotCor = XrotCor.astype('int') projMatrix = np.zeros((imageLen, imageLen)) m0, m1 = np.where((XrotCor >= 0) & (XrotCor <= (imageLen - 1))) s = sinogram[:, n] # get projection projMatrix[m0, m1] = s[XrotCor[m0, m1]] # backproject in-bounds data reconMatrix += projMatrix im = Image.fromarray((reconMatrix - np.min(reconMatrix)) / np.ptp(reconMatrix) * 255)

## Slide 7: Filter back projection
filter
ramp filter
FFT
IFFT

## Slide 8: Filter back projection
for i in range(numAngles): projfft = DFT.DFT_one(sino[:, i]) # Filter filtProj = projfft * filt filtSino[:, i] = np.real(DFT.iDFT_one(filtProj))

## Slide 9: GUI design
User interface for computed tomography reconstruction
Develop Environment :
Python +Matplotlib + Pyqt5 + Qt designer

## Slide 10
Processing message + Error message
Only back projection or
Filter back projection
Enter a line y =? , Make Numerical comparison of the true and the reconstructed values

## Slide 11
Import File (phantom)

## Slide 12
Radon Transform

## Slide 13
Reconstruction

## Slide 15: Thank you